## Slide 1: Datatypes II
Chapter 2

## Slide 2: Outline
Logical Operations on Bits
  AND, OR, NOT, XOR, (NAND, NOR)
Other Representations
  Bit vectors
  Floating Point
  ASCII
  Hexadecimal
  Octal

## Slide 3
AND | 0 | 1
0 |  | 
1 |  | 

## Slide 4
AND | 0 | 1
0 | 0 | 0
1 | 0 | 1

## Slide 5
A | B | A AND B A & B AB
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
Truth Table

## Slide 6
A | B | A AND B A & B AB
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Truth Table

## Slide 7: Bitwise AND
0101 AND 0110 (5 & 6)
0101
0110
0100

## Slide 8
A | B | A OR B A ¦ B A + B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 9
A | B | A OR B A ¦ B A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 10: Bitwise OR
0101 OR 0110 (5 | 6)
0101
0110
0111

## Slide 11
A | NOT A ~A A’
0 | 
1 | 

## Slide 12
A | NOT A ~A A’
0 | 1
1 | 0

## Slide 13: Bitwise NOT (Complement)
NOT 0101 ~5
0101
1010

## Slide 14
A | B | A XOR B A ^ B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 15
A | B | A XOR B A ^ B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 16
A | B | A XOR B A ^ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 17: Bitwise XOR
0101 XOR 0110 5^6
0101
0110
0011

## Slide 18
A | B | A NAND B ~(A & B)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 19
A | B | A NAND B ~(A & B)
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 20: Bitwise NAND
0101 NAND 0110 No C Operator
~(5 & 6)
0101
0110
1011

## Slide 21
A | B | A NOR B ~(A ¦ B)
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 22
A | B | A NOR B ~(A ¦ B)
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0

## Slide 23: Bitwise NOR
0101 NOR 0110 No C Operator
~(5 | 6)
0101
0110
1000

## Slide 24: How Many?
How many boolean functions do you think there are?
How can you prove it?

## Slide 25: All the Boolean Functions?
P | Q | FALSE | P AND Q | ~(P -> Q) P AND ~Q | P | ~(Q -> P) ~P AND Q | Q | P != Q P XOR Q | P OR Q
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
P | Q | P NOR Q | P == Q P XNOR Q | ~Q | Q -> P P OR ~Q | ~P | P -> Q ~P OR Q | P NAND Q | TRUE
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1

## Slide 26: Left Shift
0101 Leftshift 10 5 << 2
Before 0101
After 0100

## Slide 27: Right Shift
0101 Rightshift 10 5 >> 2
Before 0101
After 0001

## Slide 28: Note Well
1101 Rightshift 10 ? >> 2
Before 1101
After 0011 or
1111

## Slide 29: How would you negate in 2’s complement using bitwise operators and the plus operator?

## Slide 30: How would you negate using bitwise operators and the plus sign?
~x+1

## Slide 31: Other Representations

## Slide 32: Bit Vectors

## Slide 33: Bit Vectors
Sometimes for reasons of space efficiency we can effectively store a group of booleans packed together in a single byte/word/etc.
0
0
1
0
0
1
0
0
7
6
5
4
3
2
1
0
Item 2 in use
Item 5 in use

## Slide 35: Bit Vectors
How do we manipulate the individual bits in the bit vector?
Example how do we set bit 6?
How do we clear bit 2?
How do we toggle a bit?
How do we test a bit?
0
0
1
0
0
1
0
0
7
6
5
4
3
2
1
0

## Slide 36: Manipulating Bits
Often we use a constant (a.k.a. mask) with a boolean function
Identity: 11112& wxyz2 == wxyz2 (clear)
  So put a zero in any bit you want to clear
    11012 & wxyz2 == wx0z2
Identity: 00002 | wxyz2 == wxyz2 (set)
  So put a one in any bit you want to set
    01002 | wxyz2 == w1yz2
Invert: 11112 ^ wxyz2 = w’x’y’z’ 2 (toggle)
  So put a one in any bit you want to toggle
    10002 ^ wxyz2 == w’xyz2

## Slide 37: More Manipulating Bits
To test a bit, clear all the rest
  00102 & wxyz2 == 00y02
  Now you can test 00y02 == 00002
To put a one in position in a mask, shift left
  1 << 3 == 10002
To put a zero in position in a mask, put a one in that position and complement
  ~(1 << 3) == 01112
  (creates as many leading ones as you need)
To put a one in position in a mask, shift left
  1 << 3 == 10002

## Slide 38: Hexadecimal & Octal

## Slide 39: Difficult
Using binary numbers is both a blessing a curse!
  One can examine directly any particular bit
  Reading, writing, etc. prone to error

## Slide 40: Solution
Turns out that mathematics has an answer for us
Group bits and assign a single digit to represent each group
How big should each group be?

## Slide 41: Use a Base That’s a Power of 2!
Base 23, a.k.a. Base 8, a.k.a. Octal!
  Use the digits 0 – 7 and group bits in 3s
  001110101001012 = 072458
  14 bits in 5 octal digits!
  And it works backwards, too!
Base 2 | 00 | 111 | 010 | 100 | 101
Base 8 | 0 | 7 | 2 | 4 | 5
Base 8 | 6 | 4 | 3 | 0 | 2
Base 2 | 110 | 100 | 011 | 000 | 010

## Slide 42: Use a Base That’s a Power of 2!
Base 24, aka Base 16, aka Hexadecimal!
  Use the digits 0 – 15 and group bits in 4s
  Oops! Digits 10-15! We’ll just use A-F.
  100011110011110000012 = 8F3C116
  And it too works backwards:
Base 2 | 1000 | 1111 | 0011 | 1100 | 0001
Base 16 | 8 | F | 3 | C | 1
Base 16 | F | 0 | 0 | D | 5
Base 2 | 1111 | 0000 | 0000 | 1101 | 0101

## Slide 43: In Java (and C)
Constant integers
  456 is decimal
  0456 is octal
  0x456 is hexadecimal
This notation often shows up instead of subscripts!

## Slide 44: ASCII

## Slide 45
What about these?
Why
two
codes?
Why
is
this
at
the
end?

## Slide 46: Fun ASCII Facts
‘A’ = 65 = 4116 = 0100 0001
‘a’ = 97 = 6116 = 0110 0001
‘0’ = 48 = 3016 = 0011 0000
‘1’ = 49 = 3116 = 0011 0001
‘2’ = 50 = 3216 = 0011 0010
…
‘9’ = 57 = 3916 = 0011 1001

## Slide 47: Fun ASCII Facts
‘A’ = 65 = 4116 = 0100 0001
Ctl-A = SOH = 1 = 116 = 0000 0001
…
‘J’ = 74 = 4A16 = 0100 1010
Ctl-J = LF = 10 = A16 = 0000 1010
…
‘M’ = 77 = 4D16 = 0100 1101
Ctl-M = CR = 13 = D16 = 0000 1101

## Slide 48: Floating Point

## Slide 49: Historically
The Indiana Legislature once passed legislation declaring that the value of  was exactly 3

## Slide 50: Historically
Initially hardware manufacturers used whatever they thought was appropriate given their market and/or technology required.
IBM, DEC, CDC, etc. each had their own formats and in fact multiple formats
Typical implementations might range from 32 up to 128 bits. Common to find multiple formats available (i.e. float and double)
1985 IEEE published Floating Point Standard
  ANSI/IEEE Standard 754-1985, Standard for Binary Floating Point Arithmetic

## Slide 51: How would you do it?

## Slide 52: Scientific Notation
-6.023 x 10-23
Sign
Normalized
Mantissa
Base
Sign of
Exponent
Exponent
?

## Slide 53: Binary Floating Point Representation
Same basic idea as scientific notation
Modifications and improvements based on a long history: IEEE-754 standard
  Precise representation at the bit level
  Precise behavior of arithmetic operations
  Efficiency (Space & Time)
  Additional requirements
    Special values: not-a-number, +/-infinity, etc.
    Correct rounding
    Sortable without FP hardware
3

## Slide 54: IEEE-754
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 1.M * 2 E-127
Sign
1 is understood
Mantissa (w/o leading 1)
Base
Exponent
31
30 23
22 0

## Slide 55: IEEE-754
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 1.M * 2 E-127
Can any of these equal 0?

## Slide 56: So how can we represent 0?
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 1.M * 2 E-127
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two
Not
A
Number

E == 0
0 < E < 255
E == 255
M==0
M!=0

## Slide 57: Can be written...
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
Not
A
Number

## Slide 58
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
0 00000000 00000000000000000000000
1 00000000 00000000000000000000000
= 0
= -0
Not
A
Number

## Slide 59: Perhaps Some Automation?
https://www.h-schmidt.net/FloatConverter/IEEE754.html

## Slide 60
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
0 11111111 00000000000000000000000
1 11111111 00000000000000000000000
= Infinity
= -Infinity
Not
A
Number

## Slide 61
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
0 11111111 00000100000000000000000
1 11111111 00100010001001010101010
= NaN
= NaN
Not
A
Number

## Slide 62
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
Not
A
Number
0 10000000 00000000000000000000000
= +1 * 2(128-127) * 1.0
= 2

## Slide 63
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
Not
A
Number
0 10000001 10100000000000000000000
1 10000001 10100000000000000000000
= +1 * 2(129-127) * 1.101
= -1 * 2(129-127) * 1.101
= 6.5
= -6.5

## Slide 64
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
Not
A
Number
0 00000001 00000000000000000000000
0 00000000 10000000000000000000000
= +1 * 2(1-127) * 1.0
= +1 * 2(-126) * 0.1
= 2(-126)
= 2(-127)
Edge case for tiny numbers: E==0 is special, so 2-126 is smallest exponent; we use underflow case for anything smaller, like 2-127; note E==0 is computed as E==1

## Slide 65
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
Not
A
Number
0 00000000 00000000000000000000001
= +1 * 2(-126) * 0.00000000000000000000001
= 2(-149) (Smallest positive value)

## Slide 66
0 11111111 00000100000000000000000 = NaN
1 11111111 00100010001001010101010 = NaN
0 11111111 00000000000000000000000 = Infinity
0 10000001 10100000000000000000000 = +1 * 2(129-127) * 1.101 = 6.5
0 10000000 00000000000000000000000 = +1 * 2(128-127) * 1.0 = 2
0 00000001 00000000000000000000000 = +1 * 2(1-127) * 1.0 = 2(-126)
0 00000000 10000000000000000000000 = +1 * 2(-126) * 0.1 = 2(-127)
0 00000000 00000000000000000000001
= +1 * 2(-126) * 0.00000000000000000000001
= 2(-149) (Smallest positive value)
0 00000000 00000000000000000000000 = 0
1 00000000 00000000000000000000000 = -0
1 10000001 10100000000000000000000 = -1 * 2(129-127) * 1.101 = -6.5
1 11111111 00000000000000000000000 = -Infinity
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M

## Slide 67
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
Not
A
Number
0 00000001 00000000000000000000000 = +1 * 2(1-127) * 1.0 = 2(-126)
Smallest positive normalized number

## Slide 68
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 2 E-127 * 1.M
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two

E == 0
0 < E < 255
E == 255
M==0
M!=0
Not
A
Number
0 00000000 11111111111111111111111
= +1 * 2(-126) * 0.11111111111111111111111
Next smallest positive number below 2-126

## Slide 69: Why not E=-127?
0 00000001 00000000000000000000000 = +1 * 2(1-127) * 1.0 = 1.0 x 2(-126)
0 00000000 11111111111111111111111
= +1 * 2(-126) * 0.11111111111111111111111
0 00000000 00001000000000000000000
= +1 + 2(-126) * 0.00001 = 2(-131)
If exponent was -127
2(-127) * 0.11111111111111111111111 or
2(-126) * 0.011111111111111111111111
Non-normalized
typically
underflow
E == 0
M!=0

## Slide 70: Conversion
In CS 1331 we noted:
float f;
int i;
f = i;
i = (int)f;
What does this imply?
  Converting floats to ints we may lose information
  Converting ints to floats we may lose information
  Converting either way we may lose information

## Slide 71
#include <stdio.h>
int main()
{
float f;
int i = 1234567897;
int j;
f = i;
j = (int)f;
printf("i = %d f = %f j = %d\n", i, f, j);
return 0;
}
$ ./demo
i = 1234567897 f = 1234567936.000000 j = 1234567936

## Slide 72: Reality
Int: 0000000000000000000000000000000
Float: 0 00000000 0000000000000000000000

## Slide 73: IEEE-754 Double
0
000...00
000000000...00000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 1.M * 2 E-1023
Sign
1 is understood
Mantissa (w/o leading 1)
Base
Exponent
0
1 11
12 63

## Slide 74: Specials
0
00000000
00000000000000000000000
s
i
g
n
exponent
mantissa (significand)
(-1)S * 1.M * 2 E-1023
Non-normalized
typically
underflow
Ordinary
Old
Numbers
0
Powers
of
Two
Not
A
Number

E == 0
0 <E< 2047
E == 2047
M==0
M!=0
0
1 11
12 63

## Slide 75: Double (64 bits)
Int: 0000000000000000000000000000000
Double: 0 000...00 000000000...0000000000
52
11
31

## Slide 76
#include <stdio.h>
int main()
{
double d;
int i = 1234567897;
int j;
d = i;
j = (int)d;
printf("i = %d d = %f j = %d\n", i, d, j);
return 0;
}
./demo
i = 1234567897 d = 1234567897.000000 j = 1234567897

## Slide 77: Comparing FP Numbers
The layout of the formula allows certain operations (like > ) to be performed with no conversion
Compare:
  3.67 x 1014
  2.89 x 1016
Note the one with the bigger exponent must be bigger. You don't need to look at the mantissa.

## Slide 78: Comparing FP Numbers
Examine signs
If different “+” number is bigger
If both “+” compare magnitudes, bigger magnitude is bigger number
If both “-” compare magnitudes, smaller magnitude is bigger number

## Slide 79: Bitwise Review
Can only be applied to integral operands
that is, char, short, int and long
(signed or unsigned)
& Bitwise AND
| Bitwise OR
^ Bitwise XOR
<< Shift Left
>> Shift Right
~ 1’s Complement (Inversion)

## Slide 80: Bitwise Quiz
1 && 2
True! (1)
1 & 2
0
x << -2 Legal?
No!
x << 2 Write it another way?
x * 4
What does right shifting do to signed vars?
depends
x = x & ~077
Sets last six bits of x to zero!

## Slide 81: Bitwise Quiz
Why is x = x & ~077 better than
x = x & 0177700
First one is independent of word length
(no extra cost...evaluated at compile time)
What does this do?
(x >> (p+1-n)) & ~(~0 << n);
/* getbits: get n bits from position p */
unsigned getbits(unsigned x, int p, int n)
{
return (x >> (p+1-n)) & ~(~0 << n);
}

## Slide 82: Why is x = x & ~077 better than x = x & 0177700
x = 1010101010101010
077 = 0000000000111111
~077 = 1111111111000000
x = 1010101010101010
~077 = 1111111111000000
1010101010000000
&

## Slide 83: Why is x = x & ~077 better than x = x & 0177700
x = 1010101010101010
0177700 = 1111111111000000
x = 1010101010101010
0177700 = 1111111111000000
1010101010000000
&

## Slide 84: But what if the word size is bigger than 16 bits?

## Slide 85: Why is x = x & ~077 better than x = x & 0177700
x = 11110000111100001010101010101010
077 = 00000000000000000000000000111111
~077 = 11111111111111111111111111000000
x = 11110000111100001010101010101010
~077 = 11111111111111111111111111000000
11110000111100001010101010000000
&

## Slide 86: Why is x = x & ~077 better than x = x & 0177700
x = 11110000111100001010101010101010
0177700 = 00000000000000001111111111000000
x = 11110000111100001010101010101010
0177700 = 00000000000000001111111111000000
00000000000000001010101010000000
&

## Slide 87: /* getbits: get n bits from position p */ unsigned getbits(unsigned x, int p, int n) { return (x >> (p+1-n)) & ~(~0 << n); }
3322222222221111111111
10987654321098765432109876543210
00101010100100101010101101010101
(x >> (p+1-n)) ==> (x >> (15+1-3))
(x >> 13)
00000000000000010101010010010101
~0
11111111111111111111111111111111
~0 << n ==> ~0 << 3
11111111111111111111111111111000
~(~0 << 3)
00000000000000000000000000000111
&

## Slide 88: Questions?