## Slide 1: Digital Logic I

## Slide 2: Outline
Transistors
Logic Gates
  NOT, OR, NOR, AND, NAND
  DeMorgan's Law
  Larger Gates
Combinational Logic Circuits
  Decoder, MUX, Full Adder, PLA,
  Logical Completeness
Basic Storage Elements
  R-S Latch, Gated D latch, Register

## Slide 3: Nomenclature
Open Switch
No current can flow
Closed Switch
Current can flow

## Slide 4: Our Story Begins

## Slide 5: Boolean Algebra

## Slide 6: Communication at a Distance

## Slide 7: Telegraph

## Slide 9: Repeater

## Slide 10: Relay
Normally
Open

## Slide 11: Relay
Normally
Closed

## Slide 13: Safety First

## Slide 14: How do we make it work?
Someone
wants to go
into store
sensor
Someone
is standing
in door
swing area
sensor
MOTOR
JUICE

## Slide 16: How do we make it work?
Someone
wants to go
into store
sensor
MOTOR
JUICE
Someone
wants to leave
store
sensor

## Slide 17: Reach Out and Touch Someone
Problem: How do you talk to someone who is very far away?

## Slide 19: Claude Shannon

## Slide 20
Claude
Shannon’s
Masters
Thesis

## Slide 22: But...
Relays are
  Slow
  Good for hundreds of thousands of cycles
  Wear out
  Big
  Noisy
So...

## Slide 23: Tubes
Diode

## Slide 24: Edison Effect (Thermionic Emission)
User:Omegatron - https://secure.wikimedia.org/wikipedia/commons/wiki/File:Edisoneffect.png

## Slide 26: Tubes
Triode

## Slide 30: Vacuum Tubes
Used as
  Switches
  Amplifiers
In
  Radio
  Television
  Stereo
  Radar
  Computers

## Slide 32: But…
Tubes are
  Hot
  High power consumption
  High voltages
  Unreliable
  Expensive
  Consist of many individual components
So...

## Slide 33: William Shockley
Born February 13, 1910 Greater London, England, UK
Died August 12, 1989 (aged 79) Stanford, California, US
Nationality American
Alma mater MIT, Caltech
Known for
  Point-contact transistor and BJT
  Shockley diode equation
  Read-Shockley equation
  Shockley–Ramo theorem
  Haynes-Shockley experiment
  Shockley–Queisser limit
Awards
  Nobel Prize in Physics (1956)
  Comstock Prize in Physics (1953)
  Oliver E. Buckley Condensed Matter Prize (1953)
  Wilheln Exner Medal (1963)
  IEEE Medal of Honor (1980)

## Slide 34: So to save money...
N
N
P
+
OFF

## Slide 35: Transistors
N
N
P
+
+
ON

## Slide 36: Different Switches
+
OFF
+
OFF
A physical switch
An electronic switch

## Slide 37: Transistors & Circuits

## Slide 38: Complementary Transistors
Gate
Source
Drain
n-Type MOS
Gate
Source
Drain
p-Type MOS

## Slide 39: Common Misconception: Digital Wires Have Just 2 States!
A wire with some designated voltage (e.g. +2.9 volts) can represent a logical 1.
A wire with some designated voltage (e.g. 0 volts or ground) can represent a logical 0.
A wire that is not connected to 2.9 volts or ground is said to be floating or in a high impedance state and its value can randomly vary from a logical 0 to 1.

## Slide 40: Transistor Comparison
2.9 volts
n-Type
(normally open)
p-Type
(normally closed)
2.9 volts
2.9 volts
2.9 volts
0 volts
0 volts
2.9 volts
? volts
2.9 volts
2.9 volts
2.9 volts
? volts
(normally)
without power
to the gate
with power
to the gate

## Slide 41: N-type MOS FET*
P-type substrate
N-type
Source
Gate
Drain
Vcc
GND
GND
*Metal Oxide Semiconductor Field Effect Transistor

## Slide 42: Gate Closed
P-type substrate
N-type
Source
Gate
Drain
Channel
-
-
-
Vcc
GND
GND

## Slide 43: Gate Open
P-type substrate
N-type
Source
Gate
Drain
Channel
-
-
-
Vcc
GND
Vcc

## Slide 45: Nomenclature
Open Switch
No current can flow
Closed Switch
Current can flow

## Slide 46
Gate
Source
Drain
N-Type MOS

## Slide 47: CircuitSim N-Type MOS
Source
Drain
Gate

## Slide 48
+
OFF

## Slide 49
+
Actually
OFF
NORMALLY OPEN
How does transistor behave
when gate is at ground?

## Slide 50
+V
+V
ON
With the supply voltage applied to the device the transistor acts like a closed or connected switch

## Slide 51
+V
OFF
Open

## Slide 52
Gate
Source
Drain
P-Type MOS

## Slide 53: CircuitSim P-Type MOS
Source
Drain
Gate

## Slide 54
+
Actually
ON
NORMALLY CLOSED
How does transistor behave
when gate is at ground?

## Slide 55
+V
+V
OFF
With the supply voltage applied to the device the transistor acts like a open or disconnected switch

## Slide 56
+V
ON
Closed

## Slide 57: Inverter (Not)

## Slide 58: CircuitSim Inverter

## Slide 59: NOR

## Slide 60: OR

## Slide 61: NAND

## Slide 62: AND

## Slide 65
Logical Operations Revisited

## Slide 66: Boolean Gate Representation

## Slide 67
NOT Gate (Inverter)

## Slide 68
NOR Gates...

## Slide 69
… OR Gates

## Slide 70
NAND and AND Gates

## Slide 71: But...
Discrete transistors
  Are still big
  Use a lot of material to build
  Use a lot of power (and hence generate a lot of heat); however smaller transistors need smaller amounts of power
  Need a lot of individual connections, all of which are prone to failure
  Are so useful that we need lots of them
So...

## Slide 72: Digital Logic: Building Blocks
The basic digital logic building blocks are available as pre-packaged self-contained integrated circuits.
These chips are fast, inexpensive and easy to work with.
Each chip contains 1-6 gates. Complicated designs can require thousands of gates and hundreds of chips.
6 NOT Gates
74HC04
4 OR Gates
74HC32
4 AND Gates
74HC08

## Slide 73: DeMorgan's Law
(A'B')' = A+B
(A'+B')' = AB
A | B | A' | B' | A'B' | (A'B')' | A'+B' | (A'+B')' | A+B | AB
0 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1

## Slide 74: Conte Bubble Theorem

## Slide 75: Larger gates
ABC
A
B
C
A
B
C
A(BC)

## Slide 76: Larger gates
ABCD
A
B
C
D
A
B
C
D
(A(B(CD)))
A
B
C
D
((AB)(CD))

## Slide 77: Larger gates
A
B
A
B
C
C
A B C (ABC)’ (AB)’ ((AB)’C)’
0 0 0 1 1 1
0 0 1 1 1 0
0 1 0 1 1 1
0 1 1 1 1 0
1 0 0 1 1 1
1 0 1 1 1 0
1 1 0 1 0 1
1 1 1 0 0 1

## Slide 78: Larger gates
A
B
A
B
C
C
A B C (ABC)’ (AB)’ AB ABC (ABC)’
0 0 0 1 1 0 0 1
0 0 1 1 1 0 0 1
0 1 0 1 1 0 0 1
0 1 1 1 1 0 0 1
1 0 0 1 1 0 0 1
1 0 1 1 1 0 0 1
1 1 0 1 0 1 0 1
1 1 1 0 0 1 1 0

## Slide 79: Fan-In and Fan-Out
Fan In 3
Fan Out 2

## Slide 80: Warning
Important concept approaching!

## Slide 81: Combinational Logic
A combination of AND, OR, NOT (plus NAND & NOR)
Same inputs always produce same output

## Slide 83: Fun!

## Slide 85: Problem
You have an n bit binary number which signifies which mole is selected. How do we electrically actuate the desired mole?
[Csim]

## Slide 86: Decoder

## Slide 87: Question
If you had a decoder with a 5 bit input (i.e. a 5 bit binary number) how many outputs would the decoder have?
  5
  10
  16
  32
  64

## Slide 88: Question
If you had a decoder with n input bits (i.e. an n bit binary number) how many outputs would the decoder have?
  2n
  n2
  2n
  Cannot determine
  4

## Slide 89: Problem
You have s signals and you want to use the logical value on one of them determined by a set of n control wires
n
m
out

## Slide 90
Multiplexers

## Slide 91: Question
The basic multiplexor has
  n outputs, n control lines, 2n inputs
  1 output, 2n control lines, n inputs
  1 output, n control lines, 2n inputs
  2n outputs, 2 control lines, n inputs
  1 output, 4 control lines, 2 inputs

## Slide 92: Problem
No one will buy your new computer design unless it can do at least some math, say, like adding!

## Slide 93: Simple Adder
A
B
OUT

## Slide 94: Half Adder
A
B
OUT
Carry OUT

## Slide 95: Full Adder
A
B
OUT
Carry IN
Carry OUT

## Slide 96: Truth
A | B | Carry In | Out | Carry Out
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 

## Slide 97: Truth
A | B | Carry In | Out | Carry Out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 98: Full Adder
Don’t really need this gate

## Slide 99: The No Thinking Method!
Go buy a full-adder IC chip from Frys.

## Slide 100: Boolean Simplification

## Slide 101: Boolean Simplification
DeMorgan’s Laws

## Slide 102: AB + A’ → B + A’
A | B | AB | A’ | AB+A’ | B+A’
0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 1 | 1

## Slide 103: Consider This Circuit
A | B | C | OUT
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0

## Slide 104: Implement the Truth Table

## Slide 105: Classic Simplification
F = A’B’C’ + A’B’C + AB’C’ + AB’C
F = A’B’(C’+C) + AB’(C’+C)
F = A’B’ + AB’
F = B’(A’+A)
F = B’

## Slide 106: Quite a Simplification, No?

## Slide 107: Something to Note
We are used to writing sum-of-products with algebraic polynomials, e.g.
  X3 + 4X2 + 2X + 12
Turns out that truth tables (and other forms) naturally yield boolean expressions in sum-of-products form, e.g.
  ABC + ABC’ + A’BC + A’B’C’
This turns out to be very convenient for implementing circuits

## Slide 108: Equivalence!
Boolean Expression
Truth Table
Combinational Circuit
Karnaugh Map
You can change between ANY of these forms without losing information!

## Slide 109: Karnaugh Maps
Resources:
http://electronics-course.com/karnaugh-map
http://www.32x8.com/circuits7

## Slide 110: Question
Can you convert
  A Karnaugh map to a combinational circuit?
  A truth table to a Karnaugh map
  A truth table to a combinational circuit?
  A Boolean expression into a Karnaugh map?
  A Boolean expression into a truth table?
  A truth table into a Boolean expression?

## Slide 111: Truth Table
A | OUT
0 | x
1 | y

## Slide 112: 1 Variable Karnaugh Map
A’ | A
What is the output if A is false? | What is the output if A is true?
What does it mean if both boxes contain 1?

## Slide 113: 1 Variable Karnaugh Map
A’ | A
x | y
What does it mean if both boxes contain 1?

## Slide 114: Map: OUT = A’
A’ | A

## Slide 115: Truth Table: OUT = A’
A | OUT
0 | 1
1 | 0

## Slide 116: Map: OUT = A’
A’ | A
1 | 0

## Slide 117: 2-Variable Truth Table
A | B | OUT
0 | 0 | X0
0 | 1 | X1
1 | 0 | X2
1 | 1 | X3

## Slide 118: 2-Variable K-Map
 | B’ | B
A’ | What is the output if both A and B are false? | What is the output if A is false and B is true?
A | What is the output if A is true and B is false? | What is the output if both A and B are true?

## Slide 119: 2-Variable K-Map
 | B’ | B
A’ | X0 | X1
A | X2 | X3

## Slide 120: Map: OUT = A’B’ + AB
 | B’ | B
A’ |  | 
A |  | 

## Slide 121: Map: OUT = A’B’ + AB
 | B’ | B
A’ | 1 | 0
A | 0 | 1
Can this expression be simplified?

## Slide 122: Map: OUT = A’B’ + AB’
 | B’ | B
A’ |  | 
A |  | 

## Slide 123: Map: OUT = A’B’ + AB’
 | B’ | B
A’ | 1 | 0
A | 1 | 0
Can this expression be simplified?

## Slide 124: Segue
Suppose you had to give a series of 3 bit codes to disarm the detonation sequence of a nuclear device you were sitting on.
There would be 8 codes and they had to go in a certain sequence picked by you.
Any deviation would result in an immediate detonation of the nuclear device
What codes in what order do you use?

## Slide 125: Classic Sequence
000
001
010
011
100
101
110
111

## Slide 126: Gray Code Sequence
000 001 011 010 110 111 101 100

## Slide 127: Optical Encoder
0
1
2
3
4
5
6
7

## Slide 128: Gray Code Optical Encoder
0
1
2
3
4
5
6
7

## Slide 129: 3-bit Gray Code
000 001 011 010 110 111 101 100

## Slide 130: 2-bit Gray Code
00 01 11 10

## Slide 131: 4-bit Gray Code
0000 0001 0011 0010 0110 0111 0101 0100 1100 1101 1111 1110 1010 1011 1001 1000

## Slide 132: 3-Variable Truth Table
A | B | C | OUT
0 | 0 | 0 | X0
0 | 0 | 1 | X1
0 | 1 | 0 | X2
0 | 1 | 1 | X3
1 | 0 | 0 | X4
1 | 0 | 1 | X5
1 | 1 | 0 | X6
1 | 1 | 1 | X7

## Slide 133: Map: A’B’C + A’BC + ABC
 | B’C’ (00) | B’C (01) | BC (11) | BC’ (10)
A’ (0) | X0 | X1 | X3 | X2
A (1) | X4 | X5 | X7 | X6

## Slide 134: Map: A’B’C + A’BC + ABC
 | B’C’ | B’C | BC | BC’
A’ | 0 | 1 | 1 | 0
A | 0 | 0 | 1 | 0
Can this expression be simplified?

## Slide 135: Map: A’B’C + A’BC + ABC
 | B’C’ | B’C | BC | BC’
A’ | 0 | 1 | 1 | 0
A | 0 | 0 | 1 | 0
Can this expression be simplified?

## Slide 136: Simplifying
A’B’C + A’BC + ABC
Result of removing a variable
A’C(B’ + B) + ABC
A’C + ABC

## Slide 137: Map: A’C + ABC
 | B’C’ | B’C | BC | BC’
A’ | 0 | 1 | 1 | 0
A | 0 | 0 | 1 | 0
Can this expression be simplified: A’C + BC

## Slide 138: Simplifying
A’B’C + A’BC + ABC
Result of removing a variable
A’C(B’ + B) + ABC
A’C + ABC
C(A’ + AB)
C(A’+B)
A’C + BC

## Slide 139: Map: A’B’C’ + ABC’ + AB’C’ + A’BC’
 | B’C’ | B’C | BC | BC’
A’ | X0 | X1 | X3 | X2
A | X4 | X5 | X7 | X6

## Slide 140: Map: A’B’C’ + ABC’ + AB’C’ + A’BC’
 | B’C’ | B’C | BC | BC’
A’ | 1 | 0 | 0 | 1
A | 1 | 0 | 0 | 1
Can this expression be simplified?

## Slide 141
Wrap!!!

## Slide 142: Map: A’B’C’ + ABC’ + AB’C’ + A’BC’
 | B’C’ | B’C | BC | BC’
A’ | 1 | 0 | 0 | 1
A | 1 | 0 | 0 | 1
Expression simplifies to C’

## Slide 143: 4-Variable Truth Table
A | B | C | D | OUT
0 | 0 | 0 | 0 | 
0 | 0 | 0 | 1 | 
0 | 0 | 1 | 0 | 
0 | 0 | 1 | 1 | 
0 | 1 | 0 | 0 | 
0 | 1 | 0 | 1 | 
0 | 1 | 1 | 0 | 
0 | 1 | 1 | 1 | 
1 | 0 | 0 | 0 | 
1 | 0 | 0 | 1 | 
1 | 0 | 1 | 0 | 
1 | 0 | 1 | 1 | 
1 | 1 | 0 | 0 | 
1 | 1 | 0 | 1 | 
1 | 1 | 1 | 0 | 
1 | 1 | 1 | 1 | 

## Slide 144: 4-Variable K-Map
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 

## Slide 145: 4-Variable Truth Table
A | B | C | D | OUT
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 146: Map: A’B’C’D’ + AB’CD’ + AB’C’D’ + A’B’CD’
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 

## Slide 147: Map: A’B’C’D’ + AB’CD’ + AB’C’D’ + A’B’CD’
 | C’D’ | C’D | CD | CD’
A’B’ | 1 |  |  | 1
A’B |  |  |  | 
AB |  |  |  | 
AB’ | 1 |  |  | 1
Can this expression be simplified?

## Slide 148: Map: A’B’C’D’ + AB’CD’ + AB’C’D’ + A’B’CD’
 | C’D’ | C’D | CD | CD’
A’B’ | 1 |  |  | 1
A’B |  |  |  | 
AB |  |  |  | 
AB’ | 1 |  |  | 1
Simplifies to B’D’

## Slide 149: Each Pair Eliminates 1 Variable
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B | 1 |  |  | 1
AB |  | 1 |  | 
AB’ |  | 1 |  | 
Simplifies to A’BD’ + AC’D

## Slide 150: Eliminates 2 Variables
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  | 1 | 1 | 
AB’ |  | 1 | 1 | 
Simplifies to AD

## Slide 151: Eliminates 3 Variables
 | C’D’ | C’D | CD | CD’
A’B’ | 1 |  |  | 1
A’B | 1 |  |  | 1
AB | 1 |  |  | 1
AB’ | 1 |  |  | 1
Simplifies to D’

## Slide 152: Eliminates 3 Variables
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B | 1 | 1 | 1 | 1
AB | 1 | 1 | 1 | 1
AB’ |  |  |  | 
Simplifies to B

## Slide 153: Don’t care: Eliminates 3 Variables
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B | 1 | 1 | 1 | 1
AB | X | 1 | 1 | 1
AB’ | X |  |  | 

## Slide 154: Five Variable
E' | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 
E | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 

## Slide 155: 6 Variable
 | F’ | F
E’ |  | 
E |  | 
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 
 | C’D’ | C’D | CD | CD’
A’B’ |  |  |  | 
A’B |  |  |  | 
AB |  |  |  | 
AB’ |  |  |  | 

## Slide 156: Same Data, Different Form
Combinational Logic Circuit
Boolean Expression
Truth Table
Karnaugh Map

## Slide 157
TRUTH
TABLE
CIRCUIT
BOOLEAN
EXPRESSION
KARNAUGH
MAP

## Slide 158: PLA/PGA
Given a truth table we can implement it using output using a series of NOT gates, AND gates and then OR gates (remember sum-of-products?)
We need 2n AND gates where n is the number of inputs
  How many rows does the truth table have?
We need one OR gate for each output
General purpose Programmable Logic Array or Programmable Gate Array devices exist for this purpose

## Slide 159
Interconnections

## Slide 160: Warning
Another big concept approaching!

## Slide 161: Combinational vs. Sequential Logic
Combinational
  Combination of AND, OR, NOT (plus NAND & NOR)
  Same inputs always produce same output
  Analogous to cheap bicycle lock
Sequential
  Requires storage elements
  Output depends on inputs plus state
  Analogous to a RLR combination lock
  Used to build memory & state machines

## Slide 162: So What is State?

## Slide 163: State or No State?

## Slide 164: Sequential Logic Circuit
Combinational
Logic Circuit
Storage
Elements
Input
Output
???

## Slide 165: Basic Storage
Consider:

## Slide 166: R/S Latch

## Slide 167: Question
What happens if both inputs to the R/S latch are 0?

## Slide 168: Gated D Latch
The RS Latch can be set or cleared but what if we want to record the value on the input?
Value of
Interest
Control
Stored
Value

## Slide 169: Gated D Latch

## Slide 170: Register
Basically an array of Gated D latches!

## Slide 171: Questions