## Slide 1: The LC-3 Part I
Chapter 5

## Slide 2: Outline
The ISA: Overview
  Memory, Registers, Instruction Set, Opcodes, Datatypes, Addressing Modes, Condition Codes
Operate Instructions
  ADD, AND, NOT
Data Movement Instructions
  PC-Relative Mode, Indirect Mode, Base+Offset Mode, Immediate Mode, Examples

## Slide 3: Road Map

## Slide 4: Question
If you don’t want the execution to proceed to the next instruction what must be changed?
  Instruction Register (IR)
  Memory Address Register (MAR)
  Memory Data Register (MDR)
  Program Counter (PC)

## Slide 5: Instruction Set Architecture
The ISA specifies all the information about the computer that the software needs to be aware of.
Who uses an ISA?
What is specified?

## Slide 6: Who uses an ISA?
Machine language programmers
Assembly language programmers
Compiler writers
High-level language programmers interested in performance, debugging, etc.

## Slide 7: What Is Specified?
Memory organization
Registers
Instruction set
  Opcodes
  Data types
  Addressing modes

## Slide 8: LC-3 Memory Organization
Address space
  16 bit addresses
  0-65535
  x0-xFFFF
Addressability
  16 bits
Word Addressable/Byte Addressable?
  Strictly word addressable with 16 bit words.

## Slide 9: LC-3 Registers
General Purpose Registers
Is the PC considered to be a GPR?
  Question:
    Yes
    No
Conventions
3

## Slide 10: LC-3 Registers
General Purpose Registers
  8 General Purpose Registers
  R0 - R7
Is the PC considered to be a GPR?
  No
Conventions
  Certain Registers will have designated purposes

## Slide 11: LC-3 Instruction Set
Instruction
  Op Code
  Operands
Instruction Set
  Op Codes
    Operate
    Data movement
    Control
  Data Types
  Addressing Modes

## Slide 12: How Many Instructions?
Lots
CISC (Complex Instruction Set Computer)
Intel X86, DEC VAX, IBM Z-series
Do as much as you can in a single instruction.
Relatively easy to write efficient machine code by hand.
Few
RISC (Reduced Instruction Set Computer)
ARM, PowerPC, MIPS, LC-3
Expose as much as you can to the compiler so that it can optimize.
Hard to write efficient machine code by hand.

## Slide 13: Terminology
Patt
Gated D Latch
Master-Slave Flip-flop
Circuitsim
Register (with level-triggered setting)
D Flip-Flop
-or-
Register (with edge-triggered setting)

## Slide 14: Meet the LC-3 Instruction Set
16-bit instructions
4 bits for opcode
How many instructions?
15 – one is reserved for future use.

## Slide 15
0001
DR
SR1
0
00
SR2
ADD+
0101
DR
SR1
0
00
SR2
AND+
0001
DR
SR1
1
imm5
ADD+
0101
DR
SR1
1
imm5
AND+
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
LD+
0010
PCoffset9
DR
LDI+
1010
PCoffset9
DR
+ Indicates instructions that modify condition codes

## Slide 16
1000
000000000000
RTI
1111
0000
trapvect8
TRAP
offset6
0110
DR
LDR+
BaseR
PCoffset9
1110
LEA+
DR
1001
111111
NOT+
DR
SR
1100
RET
000
111
000000
0011
SR
ST
PCoffset9
1011
STI
SR
PCoffset9
0111
BaseR
STR
SR
offset6
1101
reserved
+ Indicates instructions that modify condition codes

## Slide 17: And the LC-3 Assembly Language
What is it?
  A symbolic representation of the binary machine language
  Instructions are one-to-one between AL and ML
  AL contains some assembler directives that start with “.”
  Assembler will look up opcodes for us
  Assembler will allow us to name memory addresses
  We’ll talk about how an assembler works a bit later

## Slide 18: Addressing Modes
Where can operands be found?
  1. In the instruction (Literal or Immediate)
  2. In registers
  3. In memory

## Slide 19: Addressing Modes
Immediate or Literal
Register
PC-relative
Indirect
Base + Offset
Each instruction usually allows a subset of addressing modes (a frequently observed characteristic of a RISC architecture)

## Slide 20
0001
DR
SR1
0
00
SR2
ADD+
0101
DR
SR1
0
00
SR2
AND+
0001
DR
SR1
1
imm5
ADD+
0101
DR
SR1
1
imm5
AND+
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
LD+
0010
PCoffset9
DR
LDI+
1010
PCoffset9
DR
+ Indicates instructions that modify condition codes
register
immediate
register
immediate
PC relative
register
PC relative
register
PC relative
indirect

## Slide 21
1000
000000000000
RTI
1111
0000
trapvect8
TRAP
offset6
0110
DR
LDR+
BaseR
PCoffset9
1110
LEA+
DR
1001
111111
NOT+
DR
SR
1100
RET
000
111
000000
0011
SR
ST
PCoffset9
1011
STI
SR
PCoffset9
0111
BaseR
STR
SR
offset6
1101
reserved
+ Indicates instructions that modify condition codes
base + offset
PC relative
register
none
none
PC relative
Indirect
base + offset
none
TBD

## Slide 22: Where’s the Operand?
Addressing Mode | Operand
Immediate | SEXT(IR[4:0])
Register | Use the contents of the specified register
PC-relative | Compute PC + SEXT(IR[8:0]) or SEXT(IR[10:0]) and dereference -- remember that PC is already incremented by this time in the instruction cycle
Indirect | Compute PC-relative address as above and dereference twice
Base + Offset | Compute specified register + SEXT(IR[5:0]) and dereference
* Dereference : Interpret what you have as a memory address and fetch

## Slide 23: Condition Codes
N - Negative
Z - Zero
P - Positive
When is the condition code register set?
  During EXECUTE when LD.CC is high
How are they used?
  There are 3 bits in the BR instruction that are ANDed with the NZP condition code bits. If any bits are on, the branch is taken

## Slide 24
+1
PC
FINITE
STATE
MACHINE
SEXT
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
INPUT
OUTPUT
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
MARMUX
ADDR2MUX
ADDR1MUX
PCMUX
+
SEXT
SEXT
ZEXT
N
Z
P
LOGIC
SEXT
16
gateMARMUX
IR
16
LD.MAR
16
gateALU
R
[10:0]
[8:0]
[5:0]
[4:0]
0
16
16
16
16
LD.CC
16
16
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
16
LD.IR
[7:0]
2
2
LD.PC
ADDR2MUX
ADDR1MUX
16
16
16
2
16
A
B
MARMUX
PCMUX

## Slide 25: Condition Code Logic

## Slide 26: Let’s Look at an Instruction
NOT
Addressing mode?
  Immediate or Literal
  Register
  PC-relative
  Indirect
  Base + Offset
An example
NOT R3,R3 1001 011 011 111111
1001
111111
NOT+
DR
SR

## Slide 27: What Makes the Fetch-Execute Cycle Happen?
The control unit.
It turns on the appropriate control signals as it steps through each state.
A more complete state diagram is in Appendix C.
It will be more understandable after Chapter 5.
18
33
35
1
6
12
32

## Slide 28: EXECUTE State for NOT
001001 ( State 9 ) 0 0 J=18
LD.REG LD.CC GateALU SR1MUX=1 ALUK=2
NOTE:
SR1MUX=1 means use IR[8:6] as SR1
(see p.574)

## Slide 29
+1
PC
FINITE
STATE
MACHINE
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
PCMUX
IR
16
LD.MAR
16
gateALU
R
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
LD.IR
2
LD.PC
16
2
16
A
B
PCMUX
INPUT
KBDR
KBSR
OUTPUT
DDR
DSR
Control
Processor
EXECUTE
3
2
3
N
Z
P
LOGIC
16
LD.CC
NOT
NOT

## Slide 30: Operate Instructions
ADD, AND
Addressing Mode?
0001
DR
SR1
0
00
SR2
ADD+
0101
DR
SR1
0
00
SR2
AND+
0001
DR
SR1
1
imm5
ADD+
0101
DR
SR1
1
imm5
AND+
  Immediate or Literal
  Register
  PC-relative
  Indirect
  Base + Offset

## Slide 31: EXECUTE States for ADD & AND
000001 ( State 1 ) 0 0 J=18
LD.REG LD.CC GateALU SR1MUX=1
000101 ( State 5 ) 0 0 J=18
LD.REG LD.CC GateALU SR1MUX=1 ALUK=1
NOTE:
SR1MUX=1 means use IR[8:6] as SR1
(see p.574)
SR2MUX select is NOT IR[5]

## Slide 32: Example
ADD R3,R3,R2
0001 011 011 000 010
ADD R3,R3,#2
0001 011 011 1 00010

## Slide 33
+1
PC
FINITE
STATE
MACHINE
SEXT
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
INPUT
OUTPUT
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
MARMUX
ADDR2MUX
ADDR1MUX
PCMUX
+
SEXT
SEXT
ZEXT
N
Z
P
LOGIC
SEXT
16
gateMARMUX
IR
16
LD.MAR
16
gateALU
R
[10:0]
[8:0]
[5:0]
[4:0]
0
16
16
16
16
LD.CC
16
16
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
16
LD.IR
[7:0]
2
2
LD.PC
ADDR2MUX
ADDR1MUX
16
16
16
2
16
A
B
MARMUX
PCMUX
3
3
2
IR[5]
0 or 1

## Slide 34: What can you do with ADD, AND and NOT

## Slide 35: What can you do with ADD, AND and NOT
Add
And
Not
Subtract
Or
Clear a register
Copy from one register to another
Increment a register by n, -16<n<15

## Slide 36: Control Instructions
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
+ Indicates instructions that modify condition codes
PC relative
register
PC relative
register
1100
RET
000
111
000000
none
Set PC to contents of BaseR
Add offset to PC if condition matches
Save PC in R7, then add PCoffset11 or set to BaseR
Set PC to contents of R7 (a.k.a. JMP R7)

## Slide 37: Data Movement Instructions
Should be read from the standpoint of the registers
  LOAD something into this register
  STORE this register into memory
In other words, STORE instructions are BACKWARDS! Read them left-to-right.

## Slide 38: Data Movement Instructions
LD+
0010
PCoffset9
DR
LDI+
1010
PCoffset9
DR
offset6
0110
DR
LDR+
BaseR
PCoffset9
1110
LEA+
DR
0011
SR
ST
PCoffset9
1011
STI
SR
PCoffset9
0111
BaseR
STR
SR
offset6

## Slide 39: Basic Format
Op
Address generation bits
DR or SR
These encode information on
how to form a 16 bit address
or a register address.
You’ll see this described as
“OP2” in the LC-3 diagrams.

## Slide 40: Data Movement Instructions
PC-Relative Addressing
LD+
0010
PCoffset9
DR
0011
SR
ST
PCoffset9
Limitations?

## Slide 41: LD Example
Addr Content Tag Op Operands
.orig x3000
3000 0015 A .fillw 21 3001 27FE LD R3,A
0010 011 1 1111 1110 LD R3 -2
What happens when we execute at x3001?

## Slide 42
+1
PC
FINITE
STATE
MACHINE
SEXT
REG
FILE
SR2 SR1
OUT OUT
MDR
MAR
MEMORY
INPUT
OUTPUT
LD.MDR
MEM.EN, R.W
GateMDR
16
16
gatePC
ALU
SR2MUX
MARMUX
ADDR2MUX
ADDR1MUX
PCMUX
+
SEXT
SEXT
ZEXT
N
Z
P
LOGIC
SEXT
16
gateMARMUX
IR
16
LD.MAR
16
gateALU
R
[10:0]
[8:0]
[5:0]
[4:0]
0
16
16
16
16
LD.CC
16
16
DR
LD.REG
SR2
3
3
16
SR1
3
16
16
16
16
LD.IR
[7:0]
2
2
LD.PC
ADDR2MUX
ADDR1MUX
16
16
16
2
16
A
B
MARMUX
PCMUX
3
1
1
1

## Slide 43: Data Movement Instructions
Base + Offset
offset6
0110
DR
LDR+
BaseR
0111
BaseR
STR
SR
offset6

## Slide 44: Data Movement Instructions
Indirect Mode
LDI+
1010
PCoffset9
DR
1011
STI
SR
PCoffset9

## Slide 45: Data Movement Instructions
Immediate Mode
PCoffset9
1110
LEA+
DR
No memory access!

## Slide 46: Compare and Contrast
LEA RD←PC + 1 + PCOffset9
LD RD←M[PC + 1 + PCOffset9]
LDI RD←M[M[PC + 1 + PCOffset9]]
LDR RD←M[RB+Offset6]

## Slide 47: Loads
LEA: Puts the address represented by some label into memory
LD: Puts the contents of some label (address) into a register
LDI: Puts the contents of memory location whose address is stored in memory at some label into a register
LDR: Puts the contents of the effective address into a register. The effective address is computed by adding the base register to the offset which is the offset6 immediate operand

## Slide 48: Stores
ST: Puts the contents of a register into an address specified by a label (address).
STI: Puts the contents of a register into a memory location whose address is stored in memory at some label
STR: Puts the contents of the source register into memory at some effective address. The effective is calculated by adding the base register to the offset6 immediate operand.

## Slide 49: A word of advice
Probably the most confusing thing for the new assembly language programmer is the confusion between memory addresses and memory contents.
Why?
Consider
int x = 10;
x = x + 2;
What exactly is x?
Is the first “x” different from the second “x”?

## Slide 50: Example
x1000
x2000
x3000
x4000
x5000
x6000
x7000
x0000
LD
0010
PCoffset9
DR
GPR's
x3000: 0010 010 000000111
x3008: 0000 0000 0000 0001
x0001
EA=x3001+x7
PC->

## Slide 51: Example
x1000
x2000
x3000
x4000
x5000
x6000
x7000
x0000
GPR's
x3000: 1010 011 000000111
x3008: 0011 0000 0001 0000
x3010: 0000 0000 0010 1010
LDI
1010
PCoffset9
DR
x002a
EA=M[x3001+x7]
EA=x3010
PC->

## Slide 52: Example
x3013: 0110 0000 0000 0000
x1000
x2000
x3010
x4000
x5000
x6000
x7000
x0000
GPR's
x3000: 0111 110 011 000011
x3010: 0000 0000 0010 1010
x3011: 0000 0000 0000 0000
x3012: 0000 0000 0000 1111
x3013: 0000 0000 1111 0000
0111
BaseR
STR
SR
offset6
EA=X3010+x3
PC->

## Slide 53: Example
x1000
x2000
x0000
x4000
x5000
x6000
x7000
x0000
GPR's
x3000: 1110 011 0 0000 1111
x3010: 0000 0000 0010 1010
x3011: 0000 0000 0000 0000
x3012: 0000 0000 0000 1111
x3013: 0000 0000 1111 0000
PCoffset9
1110
LEA+
DR
x3010
EA=x3001+xF
PC->

## Slide 54: Example
Opcodes
ADD 0x1
LEA 0xE
ST 0x3
AND 0x5
STR 0x7
LDI 0xA
LEA R1,#-3
ADD R2,R1,#14
ST R2,#-5
AND R2,R1,#0
ADD R2,R2,#5
STR R2,R1,14
LDI R3,#-9
R1 R2 R3 x30f4 x3102
x30f4 - - - -
x3102
x3102
0
5
5
5

## Slide 55: Questions?

## Slide 56: LC-3 as a Finite State Machine p. 568, Fig C.3

## Slide 57: Diagrams From Patt
P. 571 Fig C.4 – the control structure
P. 584 Fig C.9 – the control store
P. 572 Table C.1 – the control store contents
P. 573 Figure C.5 – the microsequencer

## Slide 58: Sequential Logic Circuit
Combinational
Logic Circuit
Storage
Elements
Input
Output

## Slide 59: The Control Structure
Microsequencer
(See diagram on subsequent slide)
Six-bit register
Control Store
(Memory)
26 X 49 bits
Control Signals (e.g. LD.PC, LD.CC, ALUK, GATE.ALU)
39 (bits 10-49)
6
6 (next state)
10 (IRD, COND[0-2], J[0-5])
INT
R
IR[15:12], IR[11]
BEN
PSR[15]
(Think “MAR for the Control Store”)

## Slide 60: The Control Structure (the way Patt shows it)
(See diagram on subsequent slide)
Next State
Where do these go??

## Slide 61: Data Path Control Signals

## Slide 62: Contents of the Control Store

## Slide 63: First Execute State for Each Opcode
State | IRD | COND |  |  |  |  |  | 
000000 ( State 0 ) | 0 | 2 | J=18 |  |  |  |  | 
000001 ( State 1 ) | 0 | 0 | J=18 | LD.REG | LD.CC | GateALU | SR1MUX=1 | 
000010 ( State 2 ) | 0 | 0 | J=25 | LD.MAR | GateMARMUX | ADDR2MUX=2 | MARMUX | 
000011 ( State 3 ) | 0 | 0 | J=23 | LD.MAR | GateMARMUX | ADDR2MUX=2 | MARMUX | 
000100 ( State 4 ) | 0 | 3 | J=20 |  |  |  |  | 
000101 ( State 5 ) | 0 | 0 | J=18 | LD.REG | LD.CC | GateALU | SR1MUX=1 | ALUK=1
000110 ( State 6 ) | 0 | 0 | J=25 | LD.MAR | GateMARMUX | ADDR1MUX | ADDR2MUX=1 | MARMUX
000111 ( State 7 ) | 0 | 0 | J=23 | LD.MAR | GateMARMUX | ADDR1MUX | ADDR2MUX=1 | MARMUX
001000 ( State 8 ) | 0 | 4 | J=36 | LD.MAR | GateALU | SR1MUX=2 | ALUK=3 | 
001001 ( State 9 ) | 0 | 0 | J=18 | LD.REG | LD.CC | GateALU | SR1MUX=1 | ALUK=2
001010 ( State 10 ) | 0 | 0 | J=24 | LD.MAR | GateMARMUX | ADDR2MUX=2 | MARMUX | 
001011 ( State 11 ) | 0 | 0 | J=29 | LD.MAR | GateMARMUX | ADDR2MUX=2 | MARMUX | 
001100 ( State 12 ) | 0 | 0 | J=18 | LD.PC | GateALU | PCMUX=1 | SR1MUX=1 | ALUK=3
001101 ( State 13 ) | 0 | 4 | J=37 | LD.MDR | LD.Priv | LD.Vector | GatePSR | VectorMUX=2
001110 ( State 14 ) | 0 | 0 | J=18 | LD.REG | LD.CC | GateMARMUX | ADDR2MUX=2 | MARMUX
001111 ( State 15 ) | 0 | 0 | J=28 | LD.MAR | GateMARMUX |  |  | 
For the other 48 states, see figurec9v2.xls on Canvas

## Slide 64: Micro-sequen-cer Control Signals

## Slide 65: Finding the Next Microinstruction
The 10 bits that determine the next state:
  IRD – a one-bit mux control that gates either IR[15:12] or the combination of COND and J back to the microsequencer as the next state
  COND[2:0] allows one bit of J[5:0] to be set based on a specific signal
  J[5:0] – a six-bit number that is the address of the next state (if not modified by COND)
000 | Unconditional | 011 | Addressing Mode
001 | Memory Ready | 100 | Privilege mode
010 | Branch | 101 | Interrupt present

## Slide 66: The Micro-Sequen-cer

## Slide 67: Fetch Stage Example
State 18 starts the fetch
  MAR <- PC
  PC <- PC + 1
  COND5 and J=33 (if interrupt go to 49)
State 33 waits for read complete
  Assert MEM.EN
  MDR <- MEM[MAR]
  COND1 and J=33 (if R go to state 35)
State 35 moves the instruction to IR
  IR <- MDR
  COND0 and J=32 so next state is 32

## Slide 68: Fetch Stage Microcode
State | IRD | CONDx |  |  |  |  | 
( State 18 ) | 0 | 5 | J=33 | LD.MAR | LD.PC | GatePC | 
( State 33 ) | 0 | 1 | J=33 | LD.MDR | MEM.EN |  | 
( State 35 ) | 0 | 0 | J=32 | LD.IR | GateMDR |  | 

## Slide 69: Branch Example
State 32 does the decode
  BEN <- IR[11] & N | IR[10] & Z | IR[9] & P
  State 32 has IRD=1 for next state
State 0 is chosen for a BRx instruction
  State 0 has J=18 and COND2 for next state
  The next state will be 18 if BEN is 0 or 22 (18 + 4) if BEN is 1
State 22 changes the PC
  PC <- PC + off9
  State has J=18 and COND0
  So next state is 18
State 18 starts the fetch cycle again

## Slide 70: Microcode for the Example
FYI, there is a single-bit BEN flip-flop with write-enable signal LD.BEN
This register is where the calculation of BEN is stored
State | IRD | CONDx |  |  |  |  | 
( State 32 ) | 1 | 0 | J=0 | LD.BEN |  |  | 
( State 0 ) | 0 | 2 | J=18 |  |  |  | 
( State 22 ) | 0 | 0 | J=18 | LD.PC | GateMARMUX | PCMUX=2 | ADDR2MUX=2

## Slide 71: Note that the state diagram shows the register transfers done in each word/state in the microcode! In other words, this is the microcode in a readable form! p. 568, Fig C.3

## Slide 72: Some Things to Notice
BR instruction has opcode 0000
  It’s execution takes us to state 0
  CS[0] has COND=010, J=010010 (i.e. the control store word 0 has the above values)
  The next state will be either 18 if BEN’ or 22 if BEN
CS[33] has COND=001, J=100001
  If memory is not ready, R’, then next state is 33 or if R, then next state is 35

## Slide 73: More Things to Note
CS[32] has IRD=1
  Next state is from 0 to 15 depending on IR[15:12]
JSR instructions, opcode 0100 starts at CS[4] with COND=011, J=010100
  Next state is 20 if IR[11]==0 or 21 if IR[11]==1
  State 21 executes PC:=PC+offset
  State 20 executes PC:=BaseR
ALUK is set to
  00 (ADD) in CS[1]
  01 (AND) in CS[5]
  10 (NOT) in CS[9]
  11 (PASSA) everywhere else

## Slide 74: Which Came First?
(a) The data path diagram
(b) The FSM graph
(c) The microcode
(d) The instruction set

## Slide 75: Questions?