## Slide 1: The LC-3 Part II
Chapter 5

## Slide 3: Outline
Control Instructions
  Conditional Branches, Example, Two Methods for Loop Control, Example, Jump Instruction, TRAP Instruction
Example: Counting Occurences of a Character
Data Path Revisited
  Basic Components, Instruction Cycle

## Slide 4: Control Instructions
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
1000
000000000000
RTI
1111
0000
trapvect8
TRAP
1100
RET
000
111
000000

## Slide 5: Conditional Branch
0000
n
z
p
PCoffset9
BR

## Slide 6: Example
Write a program to be located at address x3000 which will sum up 12 integers located in memory addresses x3100-x310B

## Slide 7
M = x3100
S = 0
C = 12
C > 0
S = S + Mem[M]
M = M + 1
C = C - 1
YES
NO

## Slide 8: An Algorithm
short Mem[65536];
int S = 0;
int M = x3100;
int C = 12;
while (C > 0) {
  S = S + Mem[M];
  C = C - 1;
  M = M + 1;
  }

## Slide 9: Turn Your Pseudo-Code Into Comments
; int S = 0;
; int M = x3100;
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }

## Slide 10: Decide Where Variables Will Be Stored
; S is R1, M is R2, C is R3
; int S = 0;
; int M = x3100;
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }

## Slide 11: int S = 0
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }

## Slide 12: int M = x3100
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  MINIT .fill x3100

## Slide 13: int C = 12
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  MINIT .fill x3100

## Slide 14: while (C > 0) {
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRNZ ENDW1
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  MINIT .fill x3100

## Slide 15: } (end of the while)
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0 ADD R3,R3,12
; while (C > 0) {
W1 ADD R3,R3,#0
BRNZ ENDW1
  ; S = S + Mem[M];
  ; C = C - 1;
  ; M = M + 1;
  ; }
  BRNZP W1
  MINIT .fill x3100
  ENDW1

## Slide 16: S = S + Mem[M]
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,12
; while (C > 0) {
W1 ADD R3,R3,#0
BRNZ ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ; M = M + 1;
  ; }
  BRNZP W1
  MINIT .fill x3100
  ENDW1

## Slide 17: C = C - 1
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRNZ ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ADD R3,R3,#-1
  ; M = M + 1;
  ; }
  BRNZP W1
  MINIT .fill x3100
  ENDW1

## Slide 18: M = M + 1
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRNZ ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ADD R3,R3,#-1
  ; M = M + 1;
  ADD R2,R2,#1
  ; }
  BRNZP W1
  MINIT .fill x3100
  ENDW1

## Slide 19: Add a Little Window Dressing
.orig x3000
; S is R1, M is R2, C is R3
; int S = 0;
AND R1,R1,#0
; int M = x3100;
LD R2,MINIT
; int C = 12;
AND R3,R3,#0
ADD R3,R3,#12
; while (C > 0) {
W1 ADD R3,R3,#0
BRNZ ENDW1
  ; S = S + Mem[M];
  LDR R4,R2,#0
  ADD R1,R1,R4
  ; C = C - 1;
  ADD R3,R3,#-1
  ; M = M + 1;
  ADD R2,R2,#1
  ; }
  BRNZP W1
  MINIT .fill x3100
  ENDW1 HALT
  .end

## Slide 20: And Some Data
.orig x3100
.fill 3
.fill 4
.fill 5
.fill 1
.fill 6
.fill 2
.fill 7
.fill 8
.fill 9
.fill 12
.fill 10
.fill 11
.end

## Slide 21: Assembly Algorithm
Pass 1
  Start with lc (location counter) set to 0
  For each line in the program
    If there is a tag, add(tag, lc) to the symbol table
    Increment lc by the amount of memory the line takes up (often one word)
Pass 2
  Start with lc set to 0
  For each line in the program
    Look up any symbol in the line and replace it with its value in the symbol table. If it’s a PC-relative address, replace the symbol with its symbol table value – (lc + 1)
    Convert the opcode to 4-bits, registers to 3-bits, and immediate/offset values to the right number of bits for the opcode
    Output the assembled words into the object file
    Increment lc by the amount of memory the line takes up

## Slide 22: What Do We Get?
Memory
Our Code
Why the line?

## Slide 23: What Do We Get? Page 2
Memory
Our Code

## Slide 24
R1 <- x3100
R3 <- 0
R2 <- 12
R2 ?= 0
R4 <- M[R1]
R3 <- R3 + R4
Increment R1
Decrement R2
NO
YES

## Slide 25
R1 <- x3100
R3 <- 0
R2 <- 12
While R2 != 0
R4 <- M[R1]
R3 <- R3 + R4
Increment R1
Decrement R2

## Slide 26: Program
x3000 R1 <- x3100
x3001 R3 <- 0
x3002 R2 <- 0
x3003 R2 <- 12
x3004 BRz x300A
x3005 R4 <- M[R1]
x3006 R3 <- R3 + R4
x3007 R1 <- R1 + 1
x3008 R2 <- R2 - 1
x3009 BRnzp x3004

## Slide 27: Program
x3000 R1 <- x3100
x3001 R3 <- 0
x3002 R2 <- 0
x3003 R2 <- 12
x3004 BRz x300A
x3005 R4 <- M[R1]
x3006 R3 <- R3 + R4
x3007 R1 <- R1 + 1
x3008 R2 <- R2 - 1
x3009 BRnzp x3004
LEA 1110001011111111
AND 0101011011100000
AND 0101010010100000
ADD 0001010010101100
BRz 0000010000000101
LDR 0110100001000000
ADD 0001011011000100
ADD 0001001001100001
ADD 0001010010111111
BRnzp 0000111111111010

## Slide 28: Loop Control
Counter
Sentinel
M <- x3100
S <- 0
V <- M[R1]
V =
Sentinel
S <- S + V
Increment M1
V <- Mem[M]
NO
YES

## Slide 29: What can we do with a BR?

## Slide 30: What can we do with a BR?
If then else
For
While
Do while
Conditional Branch
Unconditional branch (BRNZP or BR)
Never branch (NOP)

## Slide 31: Code Templates
Do you always have to write all the code from scratch?
Do you think the code for if/then is very similar each time you write it?
What about while, for, and do?
So why shouldn’t we make some templates instead of reinventing the wheel each time?
Using template will make your life easier

## Slide 32: if (R1>0) then .. else ..
ADD R1,R1,#0; if (R1>0) then
BRNZ ELSE1
…[THEN part]…
BRNZP ENDIF1
ELSE1 NOP ; else
…[ELSE part]…
ENDIF1 NOP ; endif

## Slide 33: for (init; R1>0; reinit)
…[initialize loop]… ; for (init;
FOR1 ADD R1,R1,#0
BRNZ ENDF1 ; R1>0;
…[FOR body]…
…[reinitialize]… ; reinit)
BRNZP FOR1
ENDF1 NOP

## Slide 34: While (R1>0)
WHILE1 ADD R1,R1.#0 ; while(R1>0)
BRNZ ENDW1
…[WHILE body]…
BRNZP WHILE1
ENDW1 NOP ; endwhile

## Slide 35: do … while (R1>0);
DO1 NOP ; do
…[DO WHILE body]…
ADD R1,R1,#0
BRP DO1 ; while(x)

## Slide 36: Example
if (a < b) {
m = 5;
} else {
m = a+1;
}

## Slide 37: Example: If – then – else
; if (a < b) {
; rewrite:if (a – b < 0)
LD R1,a
LD R2,b
NOT R2,R2
ADD R2,R2,#1
ADD R1,R1,R2
BRZP EL1
; m = 5;
AND R1,R1,#0
ADD R1,R1,#5
ST R1,m
BR EIF1
;} else {
EL1 NOP
; m = a+1;
LD R1,a
ADD R1,R1,#1
ST R1,m
;}
EIF1 NOP

## Slide 38: Example: For
for (I = 0; I < 10; I = I + 1) {
J = J + I;
}

## Slide 39: Example: For
;for (I = 0; I < 10; I = I + 1) {
; init: I = 0
AND R1,R1,#0
ST R1,I
; test (I – 10 < 0)
FOR1 LD R1,I
ADD R1,R1,#-10
BZP EFOR1
; J = J + I;
LD R1,I
LD R2,J
ADD R2,R2,R1
ST R2,J
; reinit I=I+1
LD R1,I
ADD R1,R1,#1
ST R1,I
;}
BR FOR1
EFOR1 NOP

## Slide 40: Example: For (saving registers)
ST R1,sv1
ST R2,sv2
;for (I = 0; I < 10; I = I + 1) {
; init: I = 0
AND R1,R1,#0
ST R1,I
; test (I – 10 < 0)
FOR1 LD R1,I
ADD R1,R1,#-10
BZP EFOR1
; J = J + I;
LD R1,I
LD R2,J
ADD R2,R2,R1
ST R2,J
; reinit I=I+1
LD R1,I
ADD R1,R1,#1
;}
BR FOR1
EFOR1 NOP
LD R1,sv1
LD R2,sv2

## Slide 41: JMP Instruction
1100
000
BaseR
000000
JMP

## Slide 42: What can we do with a JMP?

## Slide 43: What can we do with a JMP?
Go To!!!!
Branch long distances!!!

## Slide 44: Differences Between BR & JMP
BRx
  Can branch on N, Z, and P conditions
  Can always branch (BR or BRNZP)
  Can never branch (NOP)
  Destination address is always PCoffset9
  Can’t branch more than -256 to 255 words
JMP
  Always branches
  Destination address always in a register
  Can branch to any memory address

## Slide 45: Questions?

## Slide 46
0001
DR
SR1
0
00
SR2
ADD+
0101
DR
SR1
0
00
SR2
AND+
0001
DR
SR1
1
imm5
ADD+
0101
DR
SR1
1
imm5
AND+
0000
n
z
p
PCoffset9
BR
1100
000
BaseR
000000
JMP
0100
1
PCoffset11
JSR
JSRR
0100
0
00
BaseR
000000
LD+
0010
PCoffset9
DR
LDI+
1010
PCoffset9
DR
+ Indicates instructions that modify condition codes

## Slide 47
1000
000000000000
RTI
1111
0000
trapvect8
TRAP
offset6
0110
DR
LDR+
BaseR
PCoffset9
1110
LEA+
DR
1001
111111
NOT+
DR
SR
1100
RET
000
111
000000
0011
SR
ST
PCoffset9
1011
STI
SR
PCoffset9
0111
BaseR
STR
SR
offset6
1101
reserved
+ Indicates instructions that modify condition codes