## Slide 1: There is nothing magical about recursion

## Slide 2: The function
int fact(int n)
{
int answer;
if(n <= 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
See fact.asm in Canvas Files>Source Code

## Slide 3: Assumptions
Stack has been initialized and R6 is pointing to the top of the stack
  What does this mean?
The (assembly language) caller has placed arguments onto the stack right to left and then called the subroutine using a JSR or a JSRR thus the return address is already in R7.
You should also assume that R5 contains the caller's Frame Pointer and when you return back to her she will want it to contain the same value for the Frame Pointer as was there when she did the call.

## Slide 4: The initial code in a function is always the same
FACT
Leftmost arg (n)
R6

## Slide 5: The initial part is always the same
FACT ADD R6, R6, -4 ; Allocate space
Leftmost arg (n)
R6

## Slide 6: The initial part is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
Leftmost arg (n)
Return Address
R6

## Slide 7: The initial part is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
Leftmost arg (n)
Return Address
Old FP
R6

## Slide 8: The initial part is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
Leftmost arg (n)
Return Address
Old FP
R6
R5

## Slide 9: The initial code is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
Leftmost arg (n)
Return Address
Old FP
answer
R6
R5
Note: The space that is being pointed to by R5 and R6 can be used to store the first temporary variable. In our example we will put “answer” there.

## Slide 10: The initial code is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
Leftmost arg (n)
Return Address
Old FP
answer
R6
R5
If there are more temporary variables we can move the stack pointer and make space for them here. In our example there are no more so we are good.

## Slide 11: The initial code is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
ADD R6, R6, -2 ; Room for 2 regs
Leftmost arg (n)
Return Address
Old FP
answer
R6
R5

## Slide 12: The initial code is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
ADD R6, R6, -2 ; Room for 2 regs
STR R0, R5, -1
Leftmost arg (n)
Return Address
Old FP
answer
Saved R0
R6
R5

## Slide 13: The initial code is always the same
FACT ADD R6, R6, -4 ; Allocate space
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
ADD R6, R6, -2 ; Room for 2 regs
STR R0, R5, -1
STR R1, R5, -2
Leftmost arg (n)
Return Address
Old FP
answer
Saved R0
Saved R1
R6
R5

## Slide 14: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
Leftmost arg (n)
Return Address
Old FP
answer
R5
Assume our function has done all it is supposed to do including calculating and storing the final result in answer.
Recall that in our example answer is just a variable.
Saved R0
Saved R1
R6

## Slide 15: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
R6

## Slide 16: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
LDR R0, R5, -1 ; Restore R0
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
To Reg
R6

## Slide 17: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
LDR R0, R5, -1 ; Restore R0
LDR R1, R5, -2 ; Restore R1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
To Reg
R6

## Slide 18: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
LDR R0, R5, -1 ; Restore R0
LDR R1, R5, -2 ; Restore R1
ADD R6, R5, 0 ; Restore SP
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1

## Slide 19: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
LDR R0, R5, -1 ; Restore R0
LDR R1, R5, -2 ; Restore R1
ADD R6, R5, 0 ; Restore SP
LDR R5, R6, 1 ; Restore FP
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
To Reg

## Slide 20: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
LDR R0, R5, -1 ; Restore R0
LDR R1, R5, -2 ; Restore R1
ADD R6, R5, 0 ; Restore SP
LDR R5, R6, 1 ; Restore FP
LDR R7, R6, 2 ; Restore RA
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
Saved R0
Saved R1
R5

## Slide 21: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
LDR R0, R5, -1 ; Restore R0
LDR R1, R5, -2 ; Restore R1
ADD R6, R5, 0 ; Restore SP
LDR R5, R6, 1 ; Restore FP
LDR R7, R6, 2 ; Restore RA
ADD R6, R6, 3 ; Pop ra,fp,lv1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
Saved R0
Saved R1
R5

## Slide 22: The ending can be always the same
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3
LDR R0, R5, -1 ; Restore R0
LDR R1, R5, -2 ; Restore R1
ADD R6, R5, 0 ; Move SP
LDR R5, R6, 1 ; Restore FP
LDR R7, R6, 2 ; Restore RA
ADD R6, R6, 3 ; Move SP
RET
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
Saved R0
Saved R1
R5

## Slide 23
int fact(int n) {
int answer;
if(n <= 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
Everything we
just did took care
of the parts
marked in red

## Slide 24
FACT ADD R6, R6, -4 ; Allocate space rv,ra,fp,lv1
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
ADD R6, R6, -2 ; Make room for saved regs
STR R0, R5, -1 ; Save R0
STR R1, R5, -2 ; Save R1 ;=================================================
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3 ;
LDR R0, R5, -1 ; Restore R0
LDR R1, R5, -2 ; Restore R1
ADD R6, R5, 0 ; Restore SP
LDR R5, R6, 1 ; Restore FP
LDR R7, R6, 2 ; Restore RA
ADD R6, R6, 3 ; Pop ra,fp,lv1
RET
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 25: What about the function body
When the code in fact starts, where is
n being stored?
FP + 4
When we enter fact(), the stack appears as it does at the right
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 26
; Set up stack frame template goes above
;if (n <= 0) {
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 27
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 28
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
NOT IN CODE

## Slide 29
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 30
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 31
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
STR R0, R5, 0
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 32
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
STR R0, R5, 0
;} else {
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 33
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
STR R0, R5, 0
;} else {
BR ENDIF1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 34
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
STR R0, R5, 0
;} else {
BR ENDIF1
; answer = n * fact(n-1);
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 35
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
STR R0, R5, 0
;} else {
BR ENDIF1
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 36
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
STR R0, R5, 0
;} else {
BR ENDIF1
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 37
; Set up stack frame template goes above
;if (n <= 0) {
LDR R0, R5, 4 ; n <= 0
BRP IFELSE1
; answer = 1;
AND R0, R0, 0
ADD R0, R0, 1
STR R0, R5, 0
;} else {
BR ENDIF1
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 38
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 39
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
n-1
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}

## Slide 40
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
n-1
R6
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
Now, how do you call a subroutine?

## Slide 41
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
JSR FACT ; fact(n-1)
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
n-1
R6
fact(n-1)

## Slide 42
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
JSR FACT ; fact(n-1)
LDR R0, R6, 0 ; R0 = rv
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
n-1
R6
fact(n-1)

## Slide 43
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
JSR FACT ; fact(n-1)
LDR R0, R6, 0 ; R0 = rv
ADD R6, R6, 2 ; Pop rv and arg1
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
R6

## Slide 44
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
JSR FACT ; fact(n-1)
LDR R0, R6, 0 ; R0 = rv
ADD R6, R6, 2 ; Pop rv and arg1
; answer = mult(n, R0)
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
R6

## Slide 45
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
JSR FACT ; fact(n-1)
LDR R0, R6, 0 ; R0 = rv
ADD R6, R6, 2 ; Pop rv and arg1
; answer = mult(n, R0)
ADD R6, R6, -1; Push R0
STR R0, R6, 0
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
fact(n-1)
R6

## Slide 46
; answer = n * fact(n-1);
; rewrite: R0 = fact(n-1);
answer = mult(n, R0);
IFELSE1 LDR R0, R5, 4 ; Push n-1
ADD R0, R0, -1
ADD R6, R6, -1
STR R0, R6, 0
JSR FACT ; fact(n-1)
LDR R0, R6, 0 ; R0 = rv
ADD R6, R6, 2 ; Pop rv and arg1
; answer = mult(n, R0)
ADD R6, R6, -1; Push R0
STR R0, R6, 0
ADD R6, R6, -1; Push n
LDR R0, R5, 4
STR R0, R6, 0
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
fact(n-1)
R6
n

## Slide 47
; answer = mult(n, R0)
ADD R6, R6, -1; Push R0
STR R0, R6, 0
ADD R6, R6, -1; Push n
LDR R0, R5, 4
STR R0, R6, 0
JSR MULT ; mult(n, R0)
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
fact(n-1)
R6
n
n*fact(n-1)

## Slide 48
; answer = mult(n, R0)
ADD R6, R6, -1; Push R0
STR R0, R6, 0
ADD R6, R6, -1; Push n
LDR R0, R5, 4
STR R0, R6, 0
JSR MULT ; mult(n, R0)
LDR R0, R6, 0 ; answer = rv
STR R0, R5, 0 ;
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
fact(n-1)
R6
n
n*fact(n-1)

## Slide 49
; answer = mult(n, R0)
ADD R6, R6, -1; Push R0
STR R0, R6, 0
ADD R6, R6, -1; Push n
LDR R0, R5, 4
STR R0, R6, 0
JSR MULT ; mult(n, R0)
LDR R0, R6, 0 ; answer = rv
STR R0, R5, 0 ;
ADD R6, R6, 3 ; Pop rv and arg1-2
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
R6

## Slide 50
; answer = mult(n, R0)
ADD R6, R6, -1; Push R0
STR R0, R6, 0
ADD R6, R6, -1; Push n
LDR R0, R5, 4
STR R0, R6, 0
JSR MULT ; mult(n, R0)
LDR R0, R6, 0 ; answer = rv
STR R0, R5, 0 ;
ADD R6, R6, 3 ; Pop rv and arg1-2
ENDIF1 NOP
; }
; Tear down stack frame template goes below
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
int fact(int n) {
int answer;
if(n == 0)
answer = 1;
else
answer = n * fact(n-1);
return answer;
}
R6

## Slide 51: Some Things to Notice in fact()
Note that in the stack frame created by the beginning template code for fact(), in the function body we only touched the local variables (a.k.a answer).
All the rest of our stack use was above that fixed stack frame and used for intermediate computations.
When fact() returns to to its caller, the ending template code will throw away all of fact()’s stack frame except the return value.
Leftmost arg (n)
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
fact(n-1)
R6
n
n*fact(n-1)
Stack frame created for the first instance of fact()
All that will be left after return

## Slide 52: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
Don’t try to memorize this control transfer. Let the abstraction of recursion cover that up for you!

## Slide 53
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 2
Big Picture

## Slide 54: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 2

## Slide 55: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 2

## Slide 56: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 2

## Slide 57: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 58: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 59: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 60: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 61: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 62: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 63: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 64: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
n = 1
n = 2

## Slide 65: Big Picture
Build Stack Frame
terminating condition - YES
BR ENDIF1
terminating condition - NO
JSR FACT
FACT
Clean up and return
Ret
ENDIF1
Caller
Note that we didn’t have to account for any of this crazy control-transfer! The stack and the calling sequence handled it automatically!
n = 1

## Slide 66
What about MULT?
; Set up stack frame template
MULT ADD R6, R6, -4; Allocate space rv,ra,fp,lv1
STR R7, R6, 2 ; Save Ret Addr
STR R5, R6, 1 ; Save Old FP
ADD R5, R6, 0 ; Copy SP to FP
ADD R6, R6, -3; Make room for saved regs
STR R0, R5, -1
STR R1, R5, -2
STR R2, R5, -3
Leftmost arg
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
R6
Rightmost arg
Saved R2
Note well that this is the same preamble code we used for fact()!

## Slide 67
; R0 = 0
AND R0, R0, 0
; R1 = arg1
LDR R1, R5, 4
; R2 = arg2
LDR R2, R5, 5
; while (R1 > 0) {
WHILE2 ADD R1, R1, 0
BRNZ ENDWHILE2
; R0 += R2
ADD R0, R0, R2
; R1 -= 1
ADD R1, R1, -1
; }
BR WHILE2
; answer = R0
ENDWHILE2 STR R0, R5, 0
Leftmost arg
Return Value
Return Address
Old FP
answer
R5
Saved R0
Saved R1
R6
Rightmost arg
Saved R1
This is the usual dumb multiply-by-adding solution.

## Slide 68
; Tear down stack frame template
LDR R0, R5, 0 ; Ret val = answer
STR R0, R5, 3 ;
LDR R0, R5, -1; Restore R0
LDR R1, R5, -2; Restore R1
LDR R1, R5, -3
ADD R6, R5, 0 ; Restore SP
LDR R5, R6, 1 ; Restore FP
LDR R7, R6, 2 ; Restore RA
ADD R6, R6, 3 ; Pop ra,fp,lv1
RET
Leftmost arg
Return Value
R5
R6
Rightmost arg
And the same postamble code we used for fact(), too!

## Slide 69: Conclusions?
If you use a well-designed calling sequence, a recursive function call looks like any other function call.
And a recursive function looks just like any other function.
So why is merely the thought of writing recursive assembly code terrifying?
Good question.
Please publish a paper if you figure it out. Lots of people would like to know the answer.

## Slide 70: Questions?