## Slide 1: Introduction to GBA

## Slide 2: Outline
Why GBA?
Von Neumann Components
  Processor/Control
  Memory
  Input
  Output
Other Goodies
Programming the GBA

## Slide 3: Why GBA?
Programming on bare metal
No operating system
Makes C seem more obvious
Slow...understand performance tradeoffs
Fun!

## Slide 4: Functional Diagram
Memory
Processor
DMA
Button
Controller
Video
Controller
Audio
Controller

## Slide 5: Functional Diagram
Memory
Processor
DMA
Button
Controller
Video
Controller
Audio
Controller
Video
Display

## Slide 6: Processor
ARM-7-TDMI 3 stage pipelined RISC processor
Very popular processor
16.78 MHz clock speed
Datatypes
  8 bit (char)
  16 bit (short)
  32 bit (int)
32 bit address space

## Slide 7: ARM-7
Large register file (31 registers/16 at a time)
  Link register
  Program Counter
Load/store architecture
Fixed length instructions
6 Modes (User + 5 types of exceptions)
Status register (Neg, Zero, Carry, Overflow)
Two instruction sets!

## Slide 8: ARM 7 Processor Apps
Audio processing in the SEGA Dreamcast
D-Link DSL-604+ Wireless ADSL Router[2]
iPod from Apple
iriver portable digital audio players (the H10 uses a chip with this processor)
Juice Box
Lego Mindstorms NXT
Most of Nokia's mobile phone range.
Nintendo DS (co-processor) and Game Boy Advance from Nintendo
PocketStation
Roomba 500 series from iRobot
Sirius Satellite Radio receivers
The main CPU in Stern Pinball S.A.M System games.
Many automobiles embed ARM7 cores.

## Slide 9: Memory
RAM
  Random Access Memory
ROM
  Read Only Memory
ROM is RAM but not all RAM is ROM
Volatile
Persistent

## Slide 10: Recall
0x1 = 1
0x10 = 16
0x100 = 256
0x1000 = 4,096
0x1 0000 = 65,536
0x10 0000 = 1,048,576 (1 M)
0x100 0000 = 16 M
0x1000 0000 = 256 M
0x1 0000 0000 = 4 G

## Slide 11: System ROM
You can't get to it!
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 12: WRAM
Internal Working RAM
Sometimes called Working RAM
On the ARM chip
Very fast
Costly
Globals, static, stack all go here by default!
Force functions?
0x03 000 000
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 13: Memory Tradeoff
COST
Speed

## Slide 14: EXRAM
External RAM
Heap (malloc)
Can force variables here
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 15: Video&Hardware
Hardware Registers
  Sound
  DMA
  etc.
Palette RAM
Video RAM
Oject Attribute Memory
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 16: Game Pak ROM
Cartridge Memory
Making an array const will put it here.
Code goes here
  main
  functions
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 17: Game Pak Flash
Cartridge Memory
Can write to this block
Could store or use sprintf, etc.
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 18: Typical C Program
Dynamic Allocation
  plus forced vars
Static/Global
Stack
s
Audio
Video
Code and Constant data
Save Game Area
00000000-00003FFFF
System ROM
16KB
02000000-0203FFFF
EXRAM
256KB
03000000-03007FFF
IWRAM
32KB
04000000
Hardware Registers
05000000-050003FFF
Palette Memory
1KB
06000000-06017FFF
Video RAM
96KB
07000000-070003FF
Object Attribute Memory
1 KB
0800000
Game Pak ROM
Wait State 0
255 Mbits (~32Mb)
0A00000
Game Pak ROM
Wait State 1
255 Mbits (~32Mb)
09FE0000
Game Pak Flash
Wait State 0
1Mbit(128KB)

## Slide 19: Input
10 buttons
  Start
  Select
  A
  B
  Left
  Right
  Up
  Down
  Left shoulder
  Right shoulder

## Slide 20: Input
One button register
1 bit per button
  0 pressed
  1 not pressed

## Slide 21: Output
240 x 160 pixel color video display screen
6 display modes
  Bit mapped
  Tiled
Hardware support for sprites
Video Memory
Video
Controller
Display

## Slide 22: Output
Sound effect generators
Direct Sound Hardware (DAC)

## Slide 23: Other Goodies
Interrupts
Timers
DMA

## Slide 24: Programming
Download and install the software from Canvas (see info from TAs)
Download tutorials
  http://www.coranac.com/tonc/text/
  (Mode 3 and DMA, sections 5 and 14)
etc.

## Slide 25: Light Up a Pixel

## Slide 26: Datatypes on the GBA
Integers
  (All can be signed, the default or unsigned)
  char (1 byte)
  short int OR short (2 bytes)
  int (4 bytes)
  long int OR long (8 bytes)
Floating Point
  float
  double

## Slide 27: An Old Friend?
Remember our friends, the device registers?
GBA has quite a few
One register controls the many video modes on the GBA
REG_DISPCTL is at 0x0400 0000
And by the way, how do we touch that device register in C? *(unsigned short *)0x0400000
or better yet #define REG_DISPCNT (*(unsigned short *)0x0400000)

## Slide 28: REG_DISPCTL
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0F
0E
0D
0C
0B
0A
09
08
07
06
05
04
03
02
01
00
Mode
BG0
BG1
BG2
BG3
Bits 0-2 Mode
  0,1,2 Tile Modes
  3, 4, 5 Bitmap Modes
For bitmapped graphics use BG2
.

## Slide 29: REG_DISPCTL
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0F
0E
0D
0C
0B
0A
09
08
07
06
05
04
03
02
01
00
Mode
BG0
BG1
BG2
BG3
Bits 0-2 Mode
  0,1,2 Tile Modes
  3, 4, 5 Bitmap Modes
For bitmapped graphics use BG2
100 0000 00112 = 0x403
100000000112 = 210 + 21 + 20 = 1024 + 2 + 1 = 1027
REG_DISPCTL = 0x403;

## Slide 30: Video Memory (in Mode 3)
Located at 0x0600 0000
Consists of 240 x 160 16-bit shorts
What is the address of the pixel at
  Row 5
  Column 8

## Slide 31: Video Memory
How do we get to the pixel at row 5, col 8?
What does this question remind you of?
240
X [5,8]
160

## Slide 32: Video Memory
Looks like a two-dimensional array stored in row major order, right?
So how do we calculate an offset from the beginning?
240
X [5,8]
160

## Slide 33: Video Memory
How about row * cols + col, i.e. offset = 5 * 240 + 8 offset = 1208
160
240
X [5,8]

## Slide 34: And What Does a Pixel Look Like?
Video Memory (in Mode 3)
How do we control the color?
What would white be?
  In Hex
  In Decimal
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0

## Slide 35: So How Do We Set That Pixel?
We know the base of video memory is 0x0600000, so unsigned short *videoBuffer = (unsigned short *)0x0600000; videoBuffer[5*240+8] = 0x7fff;
Could we also say *(videoBuffer + 5*240+8) = 32767;

## Slide 36: What About LC-3 Assembly?
We have to make the assumption that LC-3 has 32-bit memory and registers, but byte addressing like the ARM
; unsigned short *videoBuffer = (unsigned short *)0x0600000; LD R0,VBADDR ST R0,videoBuffer ; videoBuffer[5*240+8] = 0x7fff; LD R0,videoBuffer LD R1,offset ADD R0,R0,R1 LD R1,WHITE STR R1,R0,#0 HALT WHITE .fill 0x7fff VBADDR .fill 0x06000000 videoBuffer .fill 0 offset .fill 2416 ; 2 x 5*240+8

## Slide 37: Pointers
Address Variables
  Variables that contain the address of other variables
Strange and beautiful syntax
  Declaring a pointer variable
  Using a pointer variable
    Storing a value in the pointer
    Storing a value in the variable being pointed to by the pointer

## Slide 38: Pointers
Putting an address into a variable
.orig x3000
LD R1 val
ST R1 ptr
HALT
val .fill x4000000
ptr .fill 0
unsigned short *ptr;
ptr = (unsigned short *)0x4000000;
Putting a value into the location contained in a pointer
.orig x3000
LD R1 ptr
LD R2 var
STR R2 R1 0
HALT
ptr .fill x4000000
var .fill 1027
LD R2 var
STI R2 addr

## Slide 39: Pointers
.orig x3000
LD R1, Value
STI R1, Dispctla
Dispctla .fill 0x4000000
Value .fill 1027

## Slide 40: C
unsigned short *ptr;
ptr = 0x4000000;
unsigned short *ptr;
ptr = 0x4000000;
*ptr = 1027;
The * operator has two meanings when used in conjunction with pointers i.e. not as the multiplication binary operator:
Used to declare a variable as a pointer (where
we must tell C what we are pointing at.
Used to dereference a pointer (i.e. We are
referring to what the pointer is pointing to as
opposed to the value of the pointer)

## Slide 41: Nota Bene
unsigned short *ptr = 0x4000000;
Same as
unsigned short *ptr;
ptr = 0x4000000;

## Slide 42: Let's Light Up a Pixel
int main(void)
{
*(unsigned short *)0x4000000 = 1027;
*(unsigned short *)0x60096F0 = 32767;
while(1)
{
}
return 0;
}

## Slide 43: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress;
int main(void)
{
pixelAddress = 0x60096F0;
REG_DISPCTL = 1027;
*pixelAddress = 32767;
while(1)
{
}
return 0;
}

## Slide 44: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0;
int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 32767;
while(1)
{
}
return 0;
}

## Slide 45: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 0x7FFF;
while(1)
{
}
return 0;
}

## Slide 46: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 0x7FFF;
while(1)
{
}
return 0;
}
Why two different ways of handling addresses?

## Slide 47: Let's Light Up a Pixel
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void)
{
REG_DISPCTL = 1027;
*pixelAddress = 0x7FFF;
pixelAddress++;
*pixelAddress = 0x1F;
*(++pixelAddress) = 0x1F<<5;
*(++pixelAddress) = 0x1F<<10;
while(1) {}
return 0;
}

## Slide 48
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *pixelAddress =
(unsigned short *) 0x60096F0; int main(void) {
REG_DISPCTL = 1027;
*pixelAddress = WHITE;
pixelAddress++;
*pixelAddress = RED;
*(++pixelAddress) = GREEN;
*(++pixelAddress) = BLUE;
while(1) {}
return 0;
}

## Slide 49: Can the fun ever stop?

## Slide 50
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *videoBuffer =
(unsigned short *)0x6000000;
int main(void) {
REG_DISPCTL = 1027;
videoBuffer[OFFSET(80,160)] = WHITE;
videoBuffer[OFFSET(80,161)] = RED;
videoBuffer[OFFSET(80,162)] = GREEN;
videoBuffer[OFFSET(80,163)] = BLUE;
while(1) {}
return 0;
}

## Slide 51: Put (almost) all this in a header file!
// myLib.h
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
unsigned short *videoBuffer =
(unsigned short *)0x6000000;

## Slide 52: Put all this in a header and a library file!
// myLib.h
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
extern unsigned short *videoBuffer;
//mylib.c
unsigned short *videoBuffer =
(unsigned short *)0x6000000;

## Slide 53
#include "myLib.h"
int main(void) {
REG_DISPCTL = 1027;
videoBuffer[OFFSET(80,160)] = WHITE;
videoBuffer[OFFSET(80,161)] = RED;
videoBuffer[OFFSET(80,162)] = GREEN;
videoBuffer[OFFSET(80,163)] = BLUE;
while(1) {}
return 0;
}

## Slide 54: Making Things Clear(er)

## Slide 55
// myLib.h
#define RGB(r,g,b) ((r)|((g)<<5)|((b)<<10))
#define OFFSET(row,col) ((row)*240+(col))
#define SETMODE(mode) REG_DISPCTL = (mode)
#define WHITE RGB(31,31,31)
#define RED(31,0,0)
#define GREEN RGB(0,31,0)
#define BLUE RGB(0,0,31)
#define REG_DISPCTL *(unsigned short *)0x4000000
#define BG2_ENABLE 0x400
#define MODE3 3
extern unsigned short *videoBuffer;
//mylib.c
unsigned short *videoBuffer =
(unsigned short *)0x6000000;

## Slide 56: REG_DISPCNT
15
14
13
12
11
10
09
08
07
06
05
04
03
02
01
00
0F
0E
0D
0C
0B
0A
09
08
07
06
05
04
03
02
01
00
Mode
BG0
BG1
BG2
BG3
Bits 0-2 Mode
  0,1,2 Tile Modes
  3, 4, 5 Bitmap Modes
For bitmapped graphics use BG2
100 0000 00112 = 0x403
100000000112 = 210 + 21 + 20 = 1024 + 2 + 1 = 1027

## Slide 57
#include "myLib.h"
int main(void) {
SETMODE(BG2_ENABLE | MODE3);
videoBuffer[OFFSET(80,160)] = WHITE;
videoBuffer[OFFSET(80,161)] = RED;
videoBuffer[OFFSET(80,162)] = GREEN;
videoBuffer[OFFSET(80,163)] = BLUE;
while(1) {}
return 0;
}

## Slide 58: Questions?